## Slide 1: DSRC Trials – Test Plan

## Slide 2: Goal : Get each car to go and park in its assigned space
Building
Assigned Parking Spaces
RSU
Tesla cars equipped with OBU
Tesla cars equipped with OBU

## Slide 3
High level view
Autopilot HW+SW
GPS (Lat, Long, UTC)
OBU
Inputs from sensors (from CAN)
Other sensors
Outputs to actuators
(to CAN)
Data extracted from WAVE messages received
We want to show that DSRC provides the non-Line Of Sight sensory dimension to the AutoPilot which none of the current sensors do! This should considerably improve the lead times for taking appropriate actions.
WAVE messages created for transmission

## Slide 4: WSMs that need to be supported
We would like to see the following WSM messages supported –
Basic Safety Message (Vehicle Safety Extension is TBD)
Intersection Collision Avoidance
Probe Vehicle Reporting
Probe Data Management
We would like to see the following applications –
Intersection Collision Warning
Forward Collision Warning

## Slide 5
If intersecting trajectories are indicated, driver is warned.
Building: Leads to Non-Line Of Sight (NLOS) communication
Intersection Collision Warning (ICA)

## Slide 6: Signals over CAN
Signals available over CAN
Steering Angle Sensor
Brake status
Vehicle Speed and Heading
Lateral and longitudinal acceleration, yaw rate information
This seems sufficient for creating the BSM.

## Slide 7: HW/SW capabilities/requirements
Is the HW we get be capable of dual channel operation ?
Would like to capture time-stamped logs for all the unicast and broadcast WSMs being exchanged between OBUs, and between an RSU and OBU(s). NOTE: Would be really helpful to be able to configure an OBU as a sniffer.
Would like to be able to configure system parameters to understand the effect on system performance (transceiver level logs, 802.11MAC and 1609.4 level logs etc.)